## Slide 1
ARCHITECTURE AND FUNCTIONAL COMPARISON
Battery Testing System
Current Platform vs Proposed “ME” Platform
From one test channel per controller to eight test channels per controller
Centralised test intelligence · one shared communication bus · unchanged PC application
Prepared for Senior Management · Technical Steering Review
Firmware Engineering · BTS-CMP-ME-001 v2.0 · 31 July 2026

## Slide 2
EXECUTIVE SUMMARY
The change in one sentence, and the three things that matter
The ME platform moves all test-sequence intelligence from the Secondary board up to the Primary board, and replaces the dedicated wired links with a single shared communication bus — turning a one-channel-per-Primary product into an eight-channel-per-Primary product.
01
Eight channels instead of one
Today one Primary controls exactly one test channel.
ME places up to eight Secondaries on one shared bus.
Roughly an eight-fold reduction in controller cost per test channel. The largest commercial driver.
02
Intelligence moves to the Primary
Today the Secondary interprets the test programme and
evaluates cutoffs. In ME it becomes a power stage.
Test logic lives in one place. New features ship as a Primary release, without touching installed Secondaries.
03
One shared bus, not dedicated links
Today each Secondary has two dedicated links.
ME shares one bus between up to eight Secondaries.
Wiring and connector counts fall sharply. In exchange, bus capacity becomes a budget we must design.
THE CENTRAL TECHNICAL QUESTION Eight Secondaries, each reporting 8 bytes every millisecond, demand exactly 1 Mbit/s of bus traffic.
That is the entire capacity of the fastest standard CAN bus, leaving nothing for anything else. Standard CAN therefore fails at any speed; CAN FD with grouped readings succeeds at about 30 % load. See slides 13 to 16.
RECOMMENDATION Proceed with the ME architecture, subject to three conditions
A · The 1 ms regulation loop stays on the Secondary. B · Protection limits stay on the Secondary, acting independently of the bus. C · Specify CAN FD and group the readings — a standard bus cannot meet the 1 ms requirement at any speed.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
2

## Slide 3
CONTENTS
What this review covers
01
Platform architecture, side by side
Three boards today, two board types proposed
02
Where the intelligence sits
The single most important architectural difference
03
Execution flow, old and new
How a test actually runs on each platform
04
Functional comparison
All twelve requirement areas mapped
05
Scaling economics
The commercial case for one Primary and eight Secondaries
06
The 1 ms live data requirement
What it asks of the bus, and the two ways the bus fails
07
Cutoff reaction time
Why complete data is not the same as fast data
08
Data volume
The storage consequence of recording every millisecond
09
Scorecard, risks and open decisions
What must be settled before work starts
Statements about the current platform describe the shipping product. ME statements are proposal requirements.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
3

## Slide 4
01 · ARCHITECTURE — CURRENT PLATFORM
OLD BTS as built today: three boards, one test channel
One clarification worth noting: the current platform is three boards, not two. The CAN interfaces already exist, on a separate COM controller.
ONE TEST CHANNEL
PC / SERVER
Web Application
Sequence authoring
Results database
→ TCP/IP — programme download
← UDP — live and session data
BMS
customer CAN network
↔ CAN
TEST BENCH HARDWARE
PRIMARY
SAM9X60 · real-time OS
───────────
• Network communication
• 4 MB serial memory
• Stores ONE programme
• Passes steps downward
• Relays measurements up
• Does NOT interpret
the test
ONE TEST CHANNEL ONLY
COM CONTROLLER
STM32H723 · bare metal
───────────
• Three CAN interfaces
• Interprets the CAN database
• BMS logging
• Industrial fieldbus
SECONDARY
STM32H723 · bare metal
───────────
• INTERPRETS every step
• EVALUATES the cutoffs
• Runs the 1 ms control loop
• 20-bit output to the
power stage
• 24-bit measurement input
• Performs calibration
───────────
The largest body of
control logic in the
whole product
BATTERY
under test
dedicated link
(UART)
test steps
dedicated link
(UART)
measurements
UART
CAN database
KEY OBSERVATION Every individual battery is given its own controller board, its own network stack and its own network address.
During a running test the Primary acts mainly as a message carrier. The complete cycle of measure, decide and act happens inside one microcontroller in about one millisecond. Fast — but it cannot scale.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
4

## Slide 5
02 · ARCHITECTURE — PROPOSED PLATFORM
NEW ME as proposed: two board types, one Primary drives eight channels
Proposal requirements. The PC application and its network protocol are preserved unchanged.
EIGHT TEST CHANNELS
PC / SERVER
Web Application
Interface UNCHANGED
→ programme download
← live and session data
TEST BENCH HARDWARE
PRIMARY TEST ENGINE
───────────
• Network communication
• Non-volatile memory
• Stores EIGHT programmes
• INTERPRETS every step
• EXECUTES the sequence
• MONITORS all cutoffs
• Controls the recording rate
• Bus master
───────────
All test logic lives here
SHARED CAN BUS
targets down
current · voltage
measurements up
current · voltage
SECONDARY 1 · node 1
Battery
SECONDARY 2 · node 2
Battery
SECONDARY 3 · node 3
Battery
SECONDARY 4 · node 4
Battery
SECONDARY 5 · node 5
Battery
SECONDARY 6 · node 6
Battery
SECONDARY 7 · node 7
Battery
SECONDARY 8 · node 8
Battery
SECONDARY
becomes
MUSCLE ONLY
Receive a target.
Regulate to it.
Report what is measured.
No step interpretation.
No test-logic cutoffs.
No cycle engine.
But it KEEPS its own
protection limits.
KEY OBSERVATION One controller, one network address and one programme store now serve eight batteries.
The saving is entirely in the controller and network layer, which is precisely where the current design is over-provisioned. The power stage count does not change — one is inherently required per battery.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
5

## Slide 6
02 · THE CORE SHIFT
Where the intelligence sits — the single most important difference
This one change drives almost every benefit and every risk in the ME proposal.
OLD BTS — DISTRIBUTED INTELLIGENCE
PRIMARY = A RELAY
Stores the programme. Hands out one step at a time.
Forwards measurements upward.
It does not interpret the test.
one step at a time
SECONDARY = BRAIN AND MUSCLE
Interprets steps · Evaluates cutoffs
Runs cycles and jumps · Calibrates
Regulates current and voltage every 1 ms
The largest single body of control logic
in the entire product
A new test feature means re-qualifying and re-programming EVERY installed Secondary.
NEW ME — CENTRALISED INTELLIGENCE
PRIMARY = THE BRAIN
Stores eight programmes · Interprets steps
Executes the sequence · Monitors cutoffs
Controls the recording rate
ALL test logic lives here
targets to eight nodes
SECONDARY × 8 = MUSCLE ONLY
Receive a target. Regulate to it.
Report what is measured.
Small, stable firmware.
A new test feature means one Primary release. One board, one qualification cycle.
WHY THIS MATTERS COMMERCIALLY Test logic becomes a single-board concern.
Today a new cutoff type or charge profile requires changing the Secondary firmware, re-qualifying it, and re-programming every Secondary already installed at a customer site. Under ME the same change is a Primary release — and once the Secondary firmware is correct, it stops changing.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
6

## Slide 7
03 · EXECUTION FLOW — CURRENT PLATFORM
OLD BTS: the measure, decide and act cycle closes inside one microcontroller
Four phases. During a running test the Primary's role is essentially to carry messages.
WHO
WHAT HAPPENS
PHASE 1 · PROGRAMME TRANSFER
Web App → Primary
Encoded test sequence, packet count, battery information
and optionally a CAN database
Primary → memory
Store the programme in its single fixed location
PHASE 2 · START AND STEP DISPATCH
Web App → Primary
Start command
Primary → Secondary
Send the FIRST step only, over the dedicated link.
The Primary does not interpret the step.
PHASE 3 · EXECUTION — ENTIRELY ON THE SECONDARY
Secondary, on its own
Interpret the step
Every 1 ms, closed on one board
Drive the power stage → measure the battery → run the
control loop → evaluate the cutoff conditions
PHASE 4 · MEASUREMENTS AND STEP ADVANCE
Secondary → Primary
Send measurements over the second dedicated link
Primary → Web App
Forward live and session data, then store in the session database
WHAT CHARACTERISES THIS DESIGN The measure, decide and act cycle takes place inside a single microcontroller, in about one millisecond.
That is exactly why the current product reacts quickly — and exactly why it cannot serve more than one channel.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
7

## Slide 8
03 · EXECUTION FLOW — PROPOSED PLATFORM
NEW ME: a two-level loop — fast and local, supervisory and central
Phases 1 and 4, which face the PC, are unchanged. Phases 2 and 3 are where the architecture changes.
WHO
WHAT HAPPENS
PHASE 1 · PROGRAMME TRANSFER — INTERFACE UNCHANGED
Web App → Primary
Encoded test sequence, packet count, battery information, optional CAN database
Primary → memory
Store in programme slot 1 to 8
PHASE 2 · START AND SEQUENCE EXECUTION — MOVED UP TO THE PRIMARY
Web App → Primary
Start command for a chosen slot and channel
Primary, for EVERY step
Interpret the step and resolve the operator, cycles, jumps and recording rate
PHASE 3 · DISTRIBUTED EXECUTION OVER THE BUS — THE TWO-LEVEL LOOP
Primary → bus → Secondary n
Target current and voltage, addressed to that node
LEVEL 1 · every 1 ms · local
Drive → measure → run the control loop → check local protection limits.
None of this touches the bus.
LEVEL 2 · over the bus
The Secondary sends grouped measurements. The Primary evaluates the
test-sequence cutoffs for channel n and updates the recording counters.
PHASE 4 · MEASUREMENTS — INTERFACE UNCHANGED
Primary → Web App
Live and session data for all eight channels
Primary, internally
Cutoff met, so advance channel n to its next step
The Primary now runs eight sequence engines at the same time. The next three slides explain what the bus can and cannot deliver in Phase 3.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
8

## Slide 9
04 · FUNCTIONAL COMPARISON (1 OF 3)
Programme authoring, transfer and storage
Requirement areas 1 to 5 and 11. The first four rows are unchanged by design, which removes a great deal of schedule risk.
PRESERVED The whole PC application and its communication protocol are unchanged.
ME is a firmware and hardware-topology change, not a rewrite of the web application. Existing session databases, reports and exports continue to work.
# | Function | OLD BTS (today) | NEW ME (proposed) | Change
1 | Sequence authoring | PC web application | PC web application | None
2 | PC to Primary connection | Ethernet | Ethernet | None
3 | Sequence transfer | Encoded, over the network | Encoded, over the network | None
4 | Data sent with the transfer | Packet count, battery information, optional CAN database | Packet count, battery information, optional CAN database | None
5 | Storage medium | 4 MB serial memory device | Non-volatile memory, to be selected | Decision needed
5 | Programme capacity | ONE sequence | EIGHT sequences | Eight-fold
11 | Slot addressing | A single fixed location; no concept of a slot | Eight addressable slots | New memory layout
MEMORY SIZING — a decision needed before board layout
The current design reserves up to 1 MB for a single test programme, on a memory device of 4 MB in total.
Eight slots at that same worst-case size would need 8 MB — more than the entire existing device.
We recommend measuring the size of real customer programmes before choosing, rather than providing for a theoretical maximum that may never occur.
WHAT THIS BUYS US
Eight batteries can be loaded with eight different test sequences and started independently, from one controller with one network address.
The operator's workflow in the web application does not change at all.
The existing investment in the PC application is fully protected.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
9

## Slide 10
04 · FUNCTIONAL COMPARISON (2 OF 3)
Execution and control — the core architectural change
Requirement areas 6, 8 and 9. This is where ownership moves from the Secondary up to the Primary.
# | Function | OLD BTS (today) | NEW ME (proposed) | Impact
6 | Step interpretation | Secondary | PRIMARY | Ownership moves up
6 | Sequence execution | Secondary | PRIMARY | Ownership moves up
6 | Step dispatch model | The Primary sends a raw step; the Secondary interprets it | The Primary interprets the step and sends only the resolved targets | The Secondary stops parsing the test protocol
9 | Cutoff monitoring | Secondary, locally, about every 1 ms | PRIMARY, using data received over the bus | Reaction time increases — see slide 16
9 | Recording rate control | Secondary | PRIMARY | Ownership moves up
8 | Secondary responsibility | A complete test engine: step interpretation, cutoffs, cycles, jumps, calibration, regulation | Regulate to a received target and report measurements | Scope greatly reduced
— | Regulation loop | Runs every 1 ms on the Secondary | MUST remain every 1 ms on the Secondary | Condition A — do not move it across the bus
WHAT WE GAIN
One place to change test logic. New operators, new cutoff types and corrections all become a Primary release.
The Secondary loses step interpretation, test-logic cutoffs and the cycle engine. Smaller firmware is easier to test and easier to trust.
Installed Secondaries no longer need re-programming when test logic changes.
WHAT WE MUST PAY FOR
Cutoff reaction slows from about 1 ms locally to about 10 ms across the bus. Acceptable for test logic, but not for protection.
A single Primary fault now affects eight channels instead of one.
Both are manageable — Conditions A and B — but neither is free. See the risk register.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
10

## Slide 11
04 · FUNCTIONAL COMPARISON (3 OF 3)
Communication, measurement reporting and scale
Requirement areas 7, 9, 10 and 12, together with the resulting scale factors.
# | Function | OLD BTS (today) | NEW ME (proposed) | Impact
7 | Primary to Secondary | A dedicated wired link, one Secondary per link | CAN, shared by up to eight nodes | Topology change
9 | Secondary to Primary | A second dedicated wired link | The same shared bus | Capacity is now shared
7 | Message content | The complete encoded step | Only the essential values: target current and voltage | Greatly simplified
10 | Node addressing | Implicit — one Secondary per link | An explicit address per node, eight in total | New addressing scheme
12 | Primary to Web Application | Live and session data over the network | Unchanged | No protocol change, but eight times the volume
RESULTING SCALE FACTORS
Secondaries
per Primary
1
OLD
8
ME
8 ×
Stored
sequences
1
OLD
8
ME
8 ×
Concurrent
test channels
1
OLD
8
ME
8 ×
Board types
in a bench
3
OLD
2
ME
one fewer
Primary boards for
eight channels
8
OLD
1
ME
−87.5 %
IMPORTANT Moving to CAN is neither a new competency nor new silicon.
• The product already ships working CAN interfaces and CAN-database handling on the separate COM controller board.
• The Primary processor already contains CAN interfaces in silicon; they are simply not enabled in the current firmware.
• The Secondary is the one board with no CAN capability today, so a transceiver and driver are genuinely new work there.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
11

## Slide 12
05 · SCALING ECONOMICS
The commercial case — controller count for an eight-channel bench
Engineering estimate. The board counts are structural; unit costs require confirmation by Purchasing.
OLD BTS — EIGHT CHANNELS = EIGHT COMPLETE STACKS
PRIM
COM
SEC
CH1
PRIM
COM
SEC
CH2
PRIM
COM
SEC
CH3
PRIM
COM
SEC
CH4
PRIM
COM
SEC
CH5
PRIM
COM
SEC
CH6
PRIM
COM
SEC
CH7
PRIM
COM
SEC
CH8
8 Ethernet ports · 8 network addresses · 24 cable runs
NEW ME — EIGHT CHANNELS = ONE PRIMARY + EIGHT STAGES
ONE PRIMARY
one shared bus
SEC
CH1
SEC
CH2
SEC
CH3
SEC
CH4
SEC
CH5
SEC
CH6
SEC
CH7
SEC
CH8
1 Ethernet port · 1 network address · 1 daisy-chained bus
Controller-side item, per eight-channel bench | OLD BTS | NEW ME | Change
Primary boards | 8 | 1 | −7
COM controller boards | 8 | 0 or 1 | −7 or −8
Secondary power-stage boards (one per battery — unchanged) | 8 | 8 | no change
Ethernet ports used | 8 | 1 | −7
Network addresses to manage | 8 | 1 | −7
Inter-board cable runs | 24 | 1 shared bus | large reduction
WHERE THE SAVING COMES FROM
The power stage count does not change, because one is inherently required per battery.
The entire saving lies in the controller and network layer.
That is precisely where the current design is over-provisioned: today every individual battery is given its own controller board, its own network stack and its own address on the customer's network.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
12

## Slide 13
06 · THE 1 MS LIVE DATA REQUIREMENT
What the requirement asks of the bus — and why a standard bus cannot deliver it
This is the most important technical slide in the deck. Every Secondary must report current and voltage every millisecond, and that data must be stored.
THE TRAFFIC PROFILE
Number of Secondaries
8
How often each one reports
every 1 ms
Size of each reading
8 bytes
Total messages per second
8,000
One message, with overhead
~125 bits
The data rate the
requirement demands
1 Mbit/s
WHAT STANDARD CAN CAN CARRY
Bus speed | Capacity | Load | Status
250 kbit/s | 250,000 bps | 400 % | Fails
500 kbit/s | 500,000 bps | 200 % | Fails
1 Mbit/s (its maximum) | 1,000,000 bps | 100–108 % | Fails
For stability, utilisation should stay below 70 %. Above 100 % the bus physically cannot move the bits fast enough to keep up with the data being produced.
THE VERDICT
Standard CAN cannot meet this requirement at any speed.
The requirement demands exactly the full capacity of the fastest standard bus, leaving nothing at all for anything else.
A SIMPLER WAY TO PICTURE IT
Think of the bus as a single-lane road with one toll booth. Every message must pass through one at a time. At 500 kbit/s each one takes 0.25 ms.
In each 1 ms window the booth can process exactly four messages — but eight Secondaries all want to send.
EIGHT SECONDARIES ALL WANT TO SEND IN THE SAME 1 ms WINDOW
1
2
3
4
5
6
7
8
THE 1 ms WINDOW — ROOM FOR ONLY FOUR
msg 1
msg 2
msg 3
msg 4
0.25 ms each · 1 ms total
LEFT WAITING
5
6
7
8
four every millisecond
The queue grows by about four messages every millisecond and never recovers. Delay rises without limit until the buffers fill and readings are lost. The bus does not simply run slowly — it fails.
SO THE OBVIOUS NEXT QUESTION IS: would a faster bus fix this?
It is worth answering carefully, because the answer determines which components we specify at hardware design time. The next slide measures all three realistic options against exactly this requirement.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
13

## Slide 14
06 · WOULD A FASTER BUS SOLVE IT?
No — but CAN FD will. Every realistic option, measured against the same requirement
Bus load required to deliver 8,000 messages per second. Anything above 100 % cannot be delivered at all, and for stability the target is below 70 %.
Chart: Bus load needed to carry the 1 ms requirement from eight Secondaries
| Standard CAN 250 kbit/s | Standard CAN 500 kbit/s | Standard CAN 1 Mbit/s (its maximum) | CAN FD with grouped readings
Bus load | 400 | 200 | 104 | 30
100 % — bus saturated
Bus option | Load | Status | Why
Standard CAN, 250 kbit/s | 400 % | Fails | Four times over capacity
Standard CAN, 500 kbit/s | 200 % | Fails | Twice over capacity
Standard CAN, 1 Mbit/s | 100–108 % | Fails | The requirement consumes the whole bus, leaving zero margin for overhead or clock drift
CAN FD, grouped readings | about 30 % | Works | Delivers every 1 ms reading with roughly 70 % of the bus still free
THE CONCLUSION
Standard CAN cannot meet a 1 ms reporting requirement for eight Secondaries at any speed.
This is not a matter of tuning or optimisation. The requirement simply exceeds what the technology can do.
CONDITION C Specify CAN FD, and settle this before hardware design begins.
This is the one decision on the critical path, because it selects the controller and transceiver and cannot be reversed cheaply afterwards. If Product Management confirms that 2 ms resolution is genuinely sufficient, standard 1 Mbit/s CAN becomes viable at about 50 % load — but that must be a deliberate decision, not a default.
AND THERE IS A SECOND, SUBTLER FAILURE — one that bites even in the most optimistic case.
Saturation is not the only problem. The next slide explains what happens when all eight Secondaries happen to transmit in the same millisecond.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
14

## Slide 15
06 · THE SECOND FAILURE MODE
Burst congestion — why one channel would silently record less data than the rest
This failure is more subtle than saturation, and it is the one most easily missed during testing.
WHAT HAPPENS
All eight Secondaries run their own 1 ms timers. Sooner or later those timers expire in the same millisecond, and all eight try to transmit at once.
On a 1 Mbit/s bus, clearing eight messages one after another takes:
8 messages × 125 bits = 1,000 bits
at 1 Mbit/s that takes exactly 1,000 microseconds = 1.0 ms
THE BURST CONSUMES THE ENTIRE CYCLE WINDOW
1 ms window
1
2
3
4
5
6
7
8
eight messages, back to back — 1,000 µs of the 1,000 µs available
next window
the next eight readings are already being produced — node 8 has not sent yet
There is no idle time left before the next round of readings arrives. Because CAN resolves collisions strictly by priority, the same lowest-priority Secondary loses every single time.
WHY THIS MATTERS FOR US SPECIFICALLY
The lowest-priority node is not an abstraction — it is a real test channel with a real customer battery on it. It would be perpetually late, miss its transmit window every cycle, and silently report less data than the other seven. That is far more damaging than an even slowdown across all eight, because it is unfair and it is easy to miss during testing.
TWO MITIGATIONS — WE RECOMMEND APPLYING BOTH
1
Group the readings
With eight readings in one message, each Secondary transmits once every 8 ms rather than eight times. The burst becomes eight messages spread across an 8 ms window instead of a 1 ms window, so the bus is idle most of the time and no node is starved.
2
Stagger the transmit timers
Give each Secondary a small fixed offset so their timers do not all expire together. This spreads the traffic evenly by design rather than relying on chance. It is inexpensive to build in now and awkward to retrofit later.
Both mitigations are firmware decisions, not hardware ones — but they must be designed in from the start.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
15

## Slide 16
06 · HOW CAN FD SOLVES IT
Group the readings — send eight in one message instead of one at a time
The Secondary still measures every millisecond. Nothing is lost. Only the way the readings travel changes.
CAN FD GIVES US TWO THINGS
1 · It carries up to 64 bytes in one message, instead of 8.
2 · It sends the data portion of the message several times faster.
STANDARD CAN — ONE READING PER MESSAGE
1
reading
1
reading
1
reading
1
reading
1
reading
1
reading
1
reading
1
reading
8 messages · 8,000 per second on the bus
CAN FD — EIGHT READINGS IN ONE MESSAGE
1
2
3
4
5
6
7
8
1 message · 1,000 per second on the bus
The Secondary measures every millisecond as before, holds the readings for a moment, then sends eight of them together. The database still receives one reading for every millisecond.
WHY GROUPING MATTERS — PART OF EVERY MESSAGE MUST STILL TRAVEL AT THE SLOWER RATE, AND THAT COST IS PAID PER MESSAGE
Approach | Data-phase speed | Messages per second | Bus load | Verdict
Standard CAN | — | 8,000 | 200 % at 500 kbit/s | Fails
CAN FD, one reading per message | 2 Mbit/s | 8,000 | about 60 % | Works, but close to the 70 % limit
CAN FD, one reading per message | 5 Mbit/s | 8,000 | about 38 % | Works
CAN FD, EIGHT readings per message | 2 Mbit/s | 1,000 | about 30 % | RECOMMENDED
CAN FD, eight readings per message | 5 Mbit/s | 1,000 | about 14 % | Works, with large margin
THE RESULT
Full 1 ms resolution at about
30 % of bus capacity — on the
cheaper 2 Mbit/s data rate.
Roughly 70 % of the bus stays free for target commands, diagnostics and urgent fault messages — and grouping also removes the burst congestion problem.
THE IMPORTANT LIMITATION Grouping readings solves the storage problem completely. It does NOT make the Primary's reaction fast.
When eight readings arrive together, the newest one in the group is already several milliseconds old. The Primary receives every reading, but it receives them a little late. Storage and protective reaction are therefore two separate problems — the next slide addresses the second one.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
16

## Slide 17
07 · CUTOFF REACTION TIME
Why complete data is not the same as fast data
A cutoff condition is a rule that ends a test step — for example, stop charging when the voltage reaches 4.2 V. Some cutoffs are test logic. Others are protection.
HOW IT WORKS TODAY
The Secondary measures the battery and checks the cutoff rules on the same board, every millisecond.
Nothing travels over a communication link. If a limit is exceeded, the Secondary reduces the drive immediately.
WHAT CHANGES IN ME
Cutoff monitoring moves to the Primary, which can only act on information that has reached it over the bus.
As the previous slides showed, that information arrives in groups roughly every 10 ms rather than continuously.
 | Today | ME, if the Primary decided alone
How often the battery is measured | every 1 ms | every 1 ms
Where the decision is made | on the same board as the measurement | on the Primary, after crossing the bus
Worst-case delay before the drive is reduced | about 1 ms | about 10 ms
FOR ORDINARY TEST LOGIC, 10 ms IS PERFECTLY ACCEPTABLE
A step that should end at 4.2 V will still end at 4.2 V. Ending it nine milliseconds later makes no measurable difference to the test result or to the customer's report.
FOR PROTECTION, 10 ms IS NOT ACCEPTABLE
If a cell is failing or a connection has come loose, current can rise very quickly. A ten-fold increase in reaction time would make ME slower to protect the battery than the product we ship today.
THE SOLUTION — SEPARATE THE TWO JOBS
1
Protection stays on the Secondary
Each Secondary keeps its own voltage, current and temperature limits and enforces them locally every millisecond, exactly as it does today. This is not new development work — the capability already exists on the board and simply needs to be retained.
2
Test logic moves to the Primary
The Primary evaluates step-ending cutoffs, cycle counts and recording using the data it receives from the bus. A granularity of about ten milliseconds is entirely appropriate for this purpose.
3
Urgent events get priority on the bus
CAN lets messages be ranked, and a higher-ranked message always goes first. A Secondary that detects a dangerous condition sends a top-priority alert, which moves ahead of all routine traffic and arrives in well under a millisecond.
THE RESULT ME matches the current product's protection speed, because protection never leaves the Secondary — while still gaining central control of the test sequence, which is the whole purpose of the change.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
17

## Slide 18
08 · A SECOND CONSEQUENCE — DATA VOLUME
Recording every millisecond is demanding for storage as well as for the bus
This deserves a deliberate product decision rather than an assumption. Figures are engineering estimates.
IF EVERY MILLISECOND IS STORED
 | Per channel | All eight channels
Readings per second | 1,000 | 8,000
Readings per hour | 3.6 million | 28.8 million
Readings in an 8-hour test | 28.8 million | 230 million
THE STORAGE COST
At roughly 40 bytes per stored reading, an eight-hour test across eight channels produces in the order of 9 GB of measurement data.
The application already writes to a separate database per test session using a background queue, so the mechanism exists — but it has never been asked to absorb eight channels at this rate.
A QUESTION WORTH ASKING BEFORE COMMITTING
Is a stored reading genuinely required for every single millisecond?
Or would 1 ms measurement combined with slower storage meet the real need?
For example, the Secondary could measure every millisecond and store every tenth reading, together with the minimum and maximum values seen in between.
That reduces stored volume by a factor of ten while preserving the extreme values — which are precisely what matter for both cutoff analysis and customer reports.
THE TWO STORAGE POLICIES COMPARED
Storage policy | Readings stored per 8-hour test | Approximate volume | What is preserved | What is lost
Store every reading | 230 million | about 9 GB | Everything | Nothing — but at high cost in disk, write load and report generation time
Store every tenth reading, plus the minimum and maximum | 23 million | about 0.9 GB | The full shape of the curve and every extreme value | Individual intermediate samples, which no customer report currently uses
THIS IS A PRODUCT DECISION, NOT AN ENGINEERING ONE — and it should be taken consciously.
The answer changes the bus specification, the database sizing and the reporting design. Deciding it early avoids reworking all three later.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
18

## Slide 19
09 · QUALITATIVE SCORECARD
Sixteen dimensions, scored 1 to 5 — engineering judgement for discussion
These are not measurements. Every score carries its justification in the accompanying document. Higher is better.
DIMENSION
OLD
NEW ME
BASIS FOR THE SCORE
Channel density and cost per channel
1
5
Eight channels per Primary instead of one
Maintainability of test logic
2
5
A Primary release, not a fleet-wide re-programme
Wiring and assembly complexity
2
5
24 cable runs become one shared bus
Board types to source and stock
2
4
Three board types reduce to two
Secondary firmware simplicity
1
5
Loses step interpretation, cutoffs, cycle engine
Speed of adding new features
2
5
No Secondary release needed per feature
Regulation loop performance
5
5
Both keep the 1 ms loop local, if Condition A holds
Protection reaction time
5
5
Equal ONLY if Condition B holds; otherwise ME scores 2
Cutoff granularity for test logic
5
3
About 1 ms today against about 10 ms on the bus
Fault isolation
5
2
One Primary fault stops 1 channel today, 8 under ME
Communication capacity margin
5
3
Dedicated links cannot contend; a shared bus can
Primary processing headroom
4
2
One Primary must run eight sequence engines
Storage capacity adequacy
4
2
Eight slots need more memory than is fitted today
Ease of diagnosis on the wire
3
4
CAN is observable with standard commercial tools
Reuse of the existing PC application
5
5
Network interfaces preserved unchanged
Reuse of existing CAN experience
3
4
CAN already ships on the COM controller
TOTAL · 16 DIMENSIONS
Dimensions stronger
50
OLD · 5
59
ME · 8
HOW TO READ THIS FAIRLY: ME wins decisively on cost, scalability and maintainability — the dimensions that determine product economics.
OLD BTS wins on fault isolation, capacity margin and processing headroom — the dimensions that determine robustness. ME is a favourable trade, not a free upgrade.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
19

## Slide 20
09 · RISK REGISTER
What must be engineered to make the trade safely
Four high risks. All four have concrete and affordable mitigations, and none is a reason to abandon the architecture.
ID | Risk | Sev | Consequence | Mitigation
R1 | Protection reaction could slow from about 1 ms to about 10 ms | HIGH safety | ME would protect the battery more slowly than the product we ship today | CONDITION B — keep independent local limits on every Secondary. The capability already exists and needs only to be retained. Verify on real hardware before release.
R2 | A single Primary fault now affects eight channels | HIGH | Eight batteries could be left in an undefined state by one failure | Each Secondary must fail safe when the bus goes quiet — no message within a set time means ramp the drive to zero. Add watchdog coverage on both boards. Fix the known memory-write fault before it serves eight channels.
R3 | Standard CAN cannot meet the 1 ms requirement — 200 % load at 500 kbit/s, over 100 % even at 1 Mbit/s | HIGH | The headline requirement of the design would not be achievable | CONDITION C — specify CAN FD and group the readings from the outset. Settle before hardware design begins. Alternatively confirm that 2 ms resolution is acceptable, making standard 1 Mbit/s CAN viable at about 50 % load.
R3a | Burst congestion starves the lowest-priority node | HIGH | One test channel would silently record less data than the other seven — an unfair failure that is easy to miss in testing | Group the readings so each Secondary transmits once every 8 ms instead of eight times, and stagger the transmit timers with a fixed per-node offset. Verify by measuring per-channel message loss on real hardware.
R4 | Bus capacity could still be exhausted as rates grow | MED | Lost readings and uneven cutoff timing | Produce a formal capacity budget at design freeze, targeting utilisation below 70 %. Rank safety and fault messages above routine traffic. Measure and report actual bus load in firmware.
R5 | The Primary may lack processing capacity for eight engines | MED | Late discovery would force a redesign or a change of processor | Carry out a load study before design freeze: run eight concurrent sequence engines with eight cutoff evaluators and eight measurement streams, then measure.
R6 | Storage memory may be undersized for eight programmes | MED | Eight full-size sequences could not be stored | Measure real customer programme sizes, then either set a limit per slot or specify a larger device. Decide before board layout.
R7 | The CAN hardware route on the Primary is not yet decided | MED | Schematic work cannot begin | Choose between the CAN interfaces already inside the Primary processor and repurposing the existing COM controller. See the next slide.
R9 | Database volume grows eightfold, and far more at 1 ms | MED | Slow reports, heavy disk use, possible data loss under load | Decide the storage policy consciously. Load-test the application at eight channels before release.
R10 | Moving the test logic could introduce errors | MED | A mature, well-proven test engine must be reproduced exactly | Port the existing logic rather than rewriting it. Build a comparison harness that runs identical sequences on both platforms and checks the results match step by step.
R1 and R2 stem from centralising the intelligence, and both are mitigated by keeping protection local to each Secondary. R3 and R3a stem from the 1 ms data rate, and both are mitigated by CAN FD with grouped readings.
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
20

## Slide 21
09 · OPEN DECISIONS
Where CAN should sit on the Primary, plus eight decisions that gate the start of work
These require answers before schematic or firmware work can begin. D2 and D3 are on the critical path.
DECISION D1 · WHERE SHOULD CAN SIT ON THE PRIMARY?
A
Use the CAN interfaces already inside the Primary processor
ADVANTAGES
The silicon capability is already present.
The COM controller can be removed entirely.
Lowest material cost of the three.
DISADVANTAGES
The driver software is new work.
The board needs pin routing and a
transceiver to be added.
B
Repurpose the COM controller as a CAN gateway
ADVANTAGES
Its CAN interfaces and database handling
already work and are proven in the field.
Keeps the BMS logging feature intact.
DISADVANTAGES
A third board type is retained.
Adds an extra hop, lengthening the
path measurements must travel.
C
Primary CAN for the test bus, COM board for the BMS bus
ADVANTAGES
Cleanly separates the safety-relevant
test bus from the customer's BMS
network. Best of both.
DISADVANTAGES
Two board types are retained.
Highest material cost of the three
options.
OUR RECOMMENDATION Option A for the test bus, retaining the COM controller only on variants that require BMS logging.
In effect this is Option C offered as a paid option rather than as standard fitment. It keeps the safety-relevant test bus on the shortest possible path while preserving the logging feature for customers who buy it.
# | Decision | Owner | Why it must be settled first
D2 | CAN FD at the full 1 ms rate, or standard CAN at a reduced 2 ms rate | Product Mgmt, with Firmware and Hardware | The decision on the critical path — it selects the controller and transceiver, and cannot be reversed cheaply after hardware design
D3 | Is a stored reading required for every millisecond? | Product Management | Closely linked to D2. If 2 ms is acceptable for storage, it is likely acceptable for the bus too
D3a | How should the eight transmit timers be staggered? | Firmware | Prevents all eight bursting in the same millisecond — cheap now, awkward to retrofit
D4 | Maximum acceptable reaction time for protection | Product and Safety | Confirms whether local limits on the Secondary are mandatory — we believe they are
D5 | Storage device and maximum programme size | Hardware and Firmware | Blocks the memory layout and the board layout
D6 | Is ME a new product line or an upgrade for installed systems? | Product Management | Existing Secondaries have no CAN interface, so an upgrade implies hardware rework
D7 | Does the BMS CAN logging feature carry forward? | Product Management | Determines whether the COM controller board survives
D8 | Must all eight channels run different sequences at once? | Product Management | Has a large effect on the processing capacity the Primary requires
BTS-CMP-ME-001 v3.0 · OLD BTS vs NEW ME · Firmware Engineering · 31 July 2026
21

## Slide 22
CONCLUSION
Five questions, five answers
Is the ME architecture the right direction?
YES
Centralising the test intelligence and moving to a shared bus converts a one-channel-per-controller product into an eight-channel-per-controller product. That is a structural improvement in unit economics and in maintainability, not an incremental one.
Can the 1 ms live data requirement be met?
YES — BUT ONLY WITH CAN FD
Eight nodes reporting 8 bytes every millisecond demand exactly 1 Mbit/s — the entire capacity of a standard CAN bus. Standard CAN therefore fails at any speed. With CAN FD and grouped readings, every reading reaches the database and the bus runs at about 30 % of capacity.
Is the change free?
NO
It reduces fault isolation, because one Primary fault now affects eight channels instead of one, and it makes the shared bus a resource that must be budgeted. These are real costs against the shipping product.
Can the trade be made safely?
YES — WITH THREE CONDITIONS
A · Keep the 1 ms regulation loop on the Secondary. B · Keep protection limits on the Secondary, acting independently of the bus. C · Specify CAN FD rather than standard CAN.
WHAT IS THE SINGLE MOST IMPORTANT THING TO GET RIGHT?
Keeping protection local to each Secondary.
Everything else in this proposal is an engineering trade-off with a cost attached. This one is a safety requirement — and it is inexpensive to honour, because the capability already exists on the board.
BTS-CMP-ME-001 v2.0 · Firmware Engineering · 31 July 2026 · Full analysis in OLD_BTS_vs_NEW_ME_Comparison.md