## Slide 1
OLD BTS · CURRENT PRODUCTION PLATFORM
Complete System and Code Functionality Map
Three boards per test channel. Every functional block that exists in the shipping product, grouped by responsibility.
ONE TEST CHANNEL
INTERFACES
PC ⟷ PRIMARY
Ethernet. TCP/IP carries the programme
and commands; UDP carries live data.
PRIMARY → SECONDARY
UART. One test step at a time,
plus start / stop / pause commands.
SECONDARY → PRIMARY
UART. Measured current, voltage,
temperature and step status.
PRIMARY ⟷ COM BOARD
UART. Carries the CAN database down
and decoded BMS signals back up.
WEB APPLICATION
PC / Server
USER INTERFACE
•
Test-sequence editor
•
Battery and programme setup
•
Live data dashboard and charts
•
Calibration screens
•
Reports and spreadsheet export
PROGRAMME PREPARATION
•
Encode the sequence into packets
•
Attach the battery information
•
Encode the CAN database (optional)
COMMUNICATION
•
Find devices on the network
•
TCP/IP client — programme, commands
•
UDP listener — live measurements
•
UDP listener — session records
•
Decode packets and check integrity
DATA STORAGE
•
Main application database
•
One database per test session
•
Background writer queue
PRIMARY
SAM9X60 · real-time operating system
NETWORK SERVICES
•
TCP/IP server — receive programme
•
UDP sender — live measurements
•
UDP sender — session records
•
Answer discovery, sync the clock
PROGRAMME STORAGE
•
Write the programme to memory
•
Fixed map — room for ONE programme
•
Store configuration and calibration
TEST FLOW — RELAY ONLY
•
Read the programme back
•
Extract ONE step at a time
•
Send that step to the Secondary
•
Pass measurements up to the PC
•
Does NOT interpret the test
BOARD LINKS
•
UART out — steps and commands
•
UART in — measurements
•
UART — CAN database to COM board
SYSTEM
•
Detect power loss, save and restore
•
Watchdog and data-integrity checks
SECONDARY
STM32H723 · bare metal
COMMAND INTERFACE
•
Receive and unpack UART frames
•
Act on start / stop / pause
•
Build the measurement frame
TEST ENGINE — ALL THE INTELLIGENCE
•
Decode the step and its operator
•
Evaluate cutoff conditions (1 ms)
•
Cycle, nesting and jump engine
•
Decide when to advance a step
•
Control the recording rate
CONTROL LOOP — EVERY 1 ms
•
Read the 24-bit measurement input
•
PID regulation — six modes
•
Write the 20-bit drive output
•
Select the measurement range
PROTECTION
•
Over-voltage, current, temperature
•
Error actions and safe shutdown
•
Watchdog
CALIBRATION
•
Two-point calibration engine
•
Store the calibration constants
COM BOARD
STM32H723 · bare metal
CAN SERVICES
•
Three CAN interfaces
•
Parse the CAN database
•
Pack and unpack signals
•
Poll devices periodically
•
Send signals up to the Primary
FIELDBUS
•
Industrial protocol slave
•
Serial line driver
CONNECTS TO
•
The customer's BMS
•
Factory fieldbus equipment
This board exists only
to serve the customer's
own CAN network.
It plays no part in
running the battery
test itself.
UART · CAN database
HOW TO READ THIS All the test intelligence sits on the Secondary. The Primary only carries messages.
The complete loop of measure, decide and act happens inside one microcontroller in about one millisecond — which is why it reacts quickly. But a whole three-board stack is needed for every single test channel, and any change to the test logic must be re-qualified and re-programmed on every Secondary already installed.
BTS-CMP-ME-001 v3.0 · System and Code Functionality Map · OLD BTS · Firmware Engineering · 31 July 2026
1

## Slide 2
NEW ME · PROPOSED PLATFORM
Complete System and Code Functionality Map
One Primary drives up to eight power stages over a single CAN FD bus. Colour shows what changes.
unchanged
moved up from the Secondary
new
retained for safety
removed
EIGHT TEST CHANNELS
INTERFACES
PC ⟷ PRIMARY
Ethernet, UNCHANGED. TCP/IP for the
programme, UDP for live data.
PRIMARY → SECONDARIES
CAN FD. Only the target current and
voltage, addressed to one of 8 nodes.
SECONDARIES → PRIMARY
CAN FD. Eight readings grouped into
one message, plus priority alerts.
SAFETY PATH
None. Protection never leaves the
Secondary board — it needs no bus.
WEB APPLICATION
PC / Server
UNCHANGED
USER INTERFACE
•
Test-sequence editor
•
Battery and programme setup
•
Live dashboard — now eight channels
•
Calibration screens
•
Reports and spreadsheet export
PROGRAMME PREPARATION
•
Encode the sequence into packets
•
Attach the battery information
•
Choose one of eight programme slots
COMMUNICATION
•
Find devices on the network
•
TCP/IP client — programme, commands
•
UDP listener — live measurements
•
UDP listener — session records
•
Decode packets and check integrity
DATA STORAGE
•
Main application database
•
One database per test session
•
Background writer — eight times the load
PRIMARY — TEST ENGINE
the brain of the system
NETWORK SERVICES · unchanged
•
TCP/IP server — receive programme
•
UDP senders — live and session data
•
Answer discovery, sync the clock
PROGRAMME STORAGE · extended
•
Store EIGHT programmes
•
Slot manager and slot selection
•
Store configuration and calibration
TEST ENGINE · MOVED UP FROM THE SECONDARY
•
Decode the step and its operator
•
Run eight sequences at the same time
•
Evaluate cutoff conditions × 8
•
Cycle, nesting and jump engine × 8
•
Control the recording rate × 8
CAN BUS MASTER · NEW
•
CAN FD driver
•
Send targets to eight node addresses
•
Receive and unpack grouped readings
•
Handle priority fault alerts first
•
Measure and report the bus load
SYSTEM · unchanged
•
Detect power loss, save and restore
•
Watchdog and data-integrity checks
ONE SHARED CAN FD BUS
SECONDARY — POWER STAGE
one per battery · eight on the bus
CAN INTERFACE · NEW
•
CAN FD driver
•
Own node address and message filter
•
Receive the target current / voltage
•
Group eight readings per message
•
Send a priority alert on a fault
CONTROL LOOP · EVERY 1 ms · unchanged
•
Read the 24-bit measurement input
•
PID regulation — six modes
•
Write the 20-bit drive output
•
Select the measurement range
PROTECTION · RETAINED — CRITICAL
•
Local over-voltage, current, temperature
•
Acts immediately, without the bus
•
Fails safe if the bus goes quiet
•
Watchdog
CALIBRATION · unchanged
•
Two-point calibration engine
NO LONGER ON THIS BOARD
×
Step decoding
×
Cutoff evaluation for test logic
×
Cycle, nesting and jump engine
×
Step-advance decisions
EIGHT NODES
Secondary 1 · Battery 1
Secondary 2 · Battery 2
Secondary 3 · Battery 3
Secondary 4 · Battery 4
Secondary 5 · Battery 5
Secondary 6 · Battery 6
Secondary 7 · Battery 7
Secondary 8 · Battery 8
Identical firmware
on every node.
Only the address
differs.
OPTIONAL
COM BOARD
Retained only on
variants that need
BMS logging over
the customer's
own CAN network.
HOW TO READ THIS All the test intelligence now sits on the Primary. The Secondary becomes a power stage — but it keeps its own protection.
One controller, one network address and one programme store serve eight batteries. Test logic changes become a Primary-only release. The 1 ms control loop and the local safety limits never leave the Secondary, so ME reacts to a fault exactly as fast as the product we ship today.
BTS-CMP-ME-001 v3.0 · System and Code Functionality Map · NEW ME · Firmware Engineering · 31 July 2026
2